INCUBATION SYSTEMS

Since 1958

| Description |  |
| --- | --- |
| Hens 9600 Ducks & Turkeys 7488 | Cabacity |
| 450 kg | Net Weigt |
| Fiber reinforced fiber glass sheets laminated to a high density styropor | Construction |
| 2 eggs trolleys each 4800 hen egg capacity | Eggs trollys |
| 64 plastic tray 72x48 cm 150 egg each | Eggs trays |
| 1 fan arms stainless pulsator by 3HP motor | Main fan |
| MECHANICAL TURNING DEVICE. | Turning |
| 1 1.4 KW isolated heater | Heating |
| humidity plastic discs system | Humidity |
| Copper coils using water at minimum 22C | Cooling |
| Digital F temp control & direct RH% reading humidity controller | Temp & humid Control |
| Control panel contains contactors &relays made by international authorized manufacturers | Control panel |
| 3 KW | Max power |
| 1.5KW/h at out side temp 25c | Power consumption |
| Alarm cases 1-Fan off 2-belt failure 3-electricity failure 4-high temperature 5-low temperature 6-low humidity 7-high humidity | alarm |

# Text boxes

فـتح الـلـه للصناعـات الهندسية

FATHALLAH ENGINEERING WORKS

S100 Specifications SETTER